## Slide 1
Ameer Effat M Elfarash
Quantification of Protein
Dept. of Genetics
Fac. of Agriculture, Assiut Univ.
aelfarash@aun.edu.eg

## Slide 3: Proteins
Make up about 15% of the cell
Have many functions in the cell
  Enzymes
  Structural
  Transport
  Motor
  Storage
  Signaling
  Receptors
  Gene regulation
  Special functions

## Slide 4
Applications
Functional Studies
Enzymatic Assays
Protein-protein interactions
Protein Ligand Interactions
Structural Studies
  Protein Crystallography
  NMR Structure Determination
Target Proteins for Rational Drug Design
Therapeutic Proteins – Preclinical Studies

## Slide 5
Expression analysis
Protein
mRNA
Real-Time PCR

## Slide 6
qRT-PCR is used to qualitatively detect gene expression
Why RT-PCR?
Gene expression analysis
  Cancer research
  Drug research
Disease diagnosis and management
  Viral quantification
Food testing
  Percent GMO food
Animal and plant breeding
  Gene copy number

## Slide 8: How does PCR work?
Log Target DNA
Cycle Number
Theoretical

## Slide 9: Real-Time PCR
Real-Time PCR a specialized technique that allows a PCR reaction to be visualized “in real time” as the reaction progresses.
Quantitative PCR relies on the principal that the quantity of target at the start of the reaction is proportional to amount of product produced during the exponential phase
∆ Fluorescence
CT
CT
Greater starting target
Less starting target
<

## Slide 10
Expression analysis
Protein Level
mRNA

## Slide 11: Protein Quantification
Most of proteins are colorless
In most cases, a mixture of several proteins or many proteins
Plasmid DNA
Bacterial DNA
Bacterial protein
Target protein

## Slide 12: Absorbance

## Slide 13: Quantification of Protein
UV absorption
Colorimetric methods
  Biuret
  Lowry
  Bradford
Other Methods

## Slide 14: UV Absorption Method
The amino acids tryptophan, tyrosine and phenylalanine absorb light in the UV wavelength (280 nm)
Since the absorption is proportional to concentration, this is a useful way to quantitate protein concentration (for proteins containing Trp)

## Slide 15: Disadvantages
If some proteins do not contain these amino acids, it will not absorb UV light.
Turbidity (cloudiness in solution) is a problem.
Nucleic acids (DNA, RNA) contaminant and phenolic acids will also absorb UV light.
Advantages:
Rapid
Non interference from ammonium sulfate.
Non destructive.

## Slide 16: Colorimetric Methods
we can modify the protein sample with appropriate reagents so as to produce a color reaction and measure protein concentration using a spectrophotometer.

## Slide 17: Advantages of Colorimetric Methods
1. Cheap
2. Not contaminating absorbance from nucleic acids!
  Biuret
  Lowry
  Bradford

## Slide 18
2.5 5 10 15 20 25 µg/mL

## Slide 20: Protein Quantification Methods
Assay method | Useful range | Comments
NanoOrange assay | 100ng/ml to 10ug/ml | Samples can be read up to six hours later without any loss in the sensitivity Low protein to protein signal variability Detection not influenced by reducing agents or nucleic acid
BCA method (Cu reduction) | 0.5ug/ml to 1.5mg.ml | Samples must be read within 10 mins Not compatible with reducing agents
Bradford assay (dye binding) | 1ug/ml to 1.5 mg/ml | Protein precipitates over time High protein to protein signal variability Not compatible with detergents
Lowry assay | 1ug/ml to 1.5mg.ml | Lengthy, multi-step procedure Not compatible with detergents, carbohydrates or reducing agents
Absorbance at 280nm | 50ng/ml to 2mg/ml | High protein to protein signal variability Detection influenced by nucleic acids and other UV absorbing contaminants

## Slide 21: Protein Assays Sensitivity
A280 (20 to 3000 ug/ml)
A205 (1 to 10 ug/ml)
Fluorescence (5 to 50 ug/ml)
Lowry method (5 to 100 ug/ml)
Bradford method (10 to 100 ug/ml)
BCA (bicinchoninic acid) method (0.5ug/ml)
Notes: Quantitative and All depend on standard curves
Non-destructive:
A280 (20 to 3000 ug/ml) trp and tyr, variable in different proteins, other things absorb eg nucleic acids
A205 (1 to 10 ug/ml) peptide bond, many other things eg buffers absorb here
Fluorescence (5 to 50 ug/ml) UV excitation leads to trp fluorescence, requires Trp and fluorometer
Destructive:
Lowry method (1 to 20 ug/200ul), Folin-Ciocalteu phenol reagent binds Tyr with CuTartrate and gives purple color; buffers, reducing agents, detergents, sugars interfere.
Bradford method (1 to 10 ug/100ul), coomassie dye binds to proteins, (Arg and aromatics); glycerol, detergents mercaptoethanol, buffers interfere.
BCA (bicinchoninic acid) method (0.5ug/ml), more stable than Lowry, but reducing agents interfere.

## Slide 22
Tools used for protein analysis
Electrophorasis
Native PAGE
Native Gradient PAGE
Urea PAGE
SDS PAGE
SDS Gradient PAGE
IEF
2D PAGE
Western Blot
Without
Electrophorasis
Cloning
Site-directed mutagenesis
protein tags
Protein structures
Proteomics
Protein Sequencing
Protein-protein interactions

## Slide 23
Cloning
Why?
Obtain pure protein
Make large quantities to facilitate study

## Slide 24: Functional Study
  DNA binding
  enzyme activity
  stability
  etc.,

## Slide 25
Protein structures

## Slide 26
The diffraction of X-ray by protein crystals can reveal a protein’s exact structure

## Slide 27: Produce Antibodies

## Slide 28
Protein tags

## Slide 30
Site-directed mutagenesis

## Slide 31: Protein Sequencing

## Slide 32: Commercial Uses